## Slide 1: Continuous Time Control of Tandem Production Lines
Mehmet Murat Fadıloğlu
Özge Büyükdağlı
Yaşar University, Izmir

## Slide 2: Content
Introduction
Literature
The Models
  Basic Model
  Model with Breakdowns
Numerical Experiments

## Slide 3: Introduction
We consider the problem of production control and stock rationing in a make-to-stock production system with several customer classes that generate independent Poisson demands.
We model the make-to-stock production system with
  A tandem production line with a finished goods buffer at the end
  Workstations with exponential production times and intermediate buffers
At decision epochs, we make
  the stock allocation decision for the finished goods and
  Production decision (continue or stop) at each workstation.

## Slide 4: Introduction
A continuous-time Markov control problem
Via uniformization technique, the problem is transformed into a discrete-time dynamic program.
We would like to
  characterize the best production/inventory policies
  compare them with simpler/applicable policies
We also consider a variation of the basic model which incorporates breakdowns and repairs at the stations.

## Slide 5: Literature
Veatch and Wein (1994) : first application of the optimal control paradigm to investigate production and inventory control in tandem lines.
  Theoretical properties of the two station problem and some numerical examples on the performance of the various pull mechanisms
Karaesmen and Dallery (2000) : performance evaluation of available pull mechanisms via mainly an experimental study.
  Close in spirit to our study
  No rationing
  Backordering environment (we use lost sales)
  We aim to consider a wider class of models (breakdowns, etc…)
  We emphasize managerial insights

## Slide 6: Models
Basic Model
Model with Breakdowns

## Slide 7: Basic Model
A production/inventory system with two workstations, an intermediate buffer between the workstations and an exit buffer in which the finished goods are kept.
Station 1
Station 2
infinite supply
Production at the first station
Production at the second station
customer
demand
Another customer
demand
Demand Arrival

## Slide 8: Basic Model State of the System
where,
: the intermediate items inventory at time , (including the item in process at station 2)
: the finished good inventory level at time
Station 1
Station 2
WIP
FG

## Slide 9: Basic Model The Events
The events that potentially change the state of the system are
  production completions at stations and
  demand arrivals
State of the system experiences
Production completion at station with rate
Production completion at station with rate
Demand arrival with 𝜆
when satisfied
when rejected

## Slide 10: Basic Model
Via uniformization technique (Lippman (1975)), we transform this continuous model to a discrete-time Markov control model.
We define the uniform rate,
w.l.o.g.,
Then, the optimal cost-to-go function;
Holding Costs
Station 1
production decision
Station 2
production decision
Rationing Decision

## Slide 11: Basic Model
where for :
Either to satisfy an arriving demand
Or reject…
No finished goods,
lost sales inevitable

## Slide 12: Model with Breakdowns
A variation on the basic model that allows random breakdowns and repairs at both stations
  The time to next breakdown
  For a station that is down, the time to repair
Station 1
Station 2
infinite supply
breakdown
breakdown
customer
demand

## Slide 13: Model with Breakdowns State of the System
System state ought to be redefined with considering the status of the stations:
Let be the indicator variable for the station state,
Then new state vector is
State Space of the System:
}

## Slide 14: Model with Breakdowns The Events
The events are:
Production completions, demand arrivals, breakdowns and repairs
Production completions
  When the station is up ()
  occurs with rate ,
  and for stations 1 and 2, respectively.
  If ,
  production completion at stationcannot occur

## Slide 15: Model with Breakdowns The Events
Demand arrivals of class j occurs with rate
  If satisfied,
  If not, system state remains the same
Station changes its state from
  up to down (breakdown occurs) with rate and
  down to up (gets repaired) with rate

## Slide 16: Model with Breakdowns
When both stations are up ():
Production decisions can be made
Breakdowns arrive
No repair occurs (self transition)
Rationing decision for a demand arrival
Holding Costs

## Slide 17: The Model with Breakdowns
Station 1 is down and station 2 is up ():
Breakdowns still arrive for the up station (2),
Repair occurs for down station (1)
No production decision can be made for down station (1)

## Slide 18: The Model with Breakdowns
Station 1 is up and station 2 is down ()
Similarly…

## Slide 19: The Model with Breakdowns
When both machines are down ()
Only breakdowns may occur in this case
Not much to decide…

## Slide 20: Numerical Experiments
Optimal policies are obtained via a value iteration algorithm implemented on MATLAB.
We use the average cost criterion that is independent of the initial state.
This also allows us using steady-state analysis for evaluating other policies as well as the optimal policy.
Policy parameters for other policies are optimized via an exhaustive search over a reasonable subset of the parameter space.

## Slide 21: Numerical Experiments
Value Iteration
Optimal Production Policy
Optimal Rationing Policy
Avg. Cost
One-Step Transition Matrix
Avg. FG
Avg. WIP
Lost Sales Rate
Avg. Cost
Setting
Steady State Analysis
Production Policy
(CONWIP, Kanban etc. )
Rationing Policy
(Static, FCFS, etc. )
Optimal Policy Parameters

## Slide 22: Numerical Experiments Basic Model with No Rationing
We consider a system with parameters
 | (FG) |  |  |  |  |  |  |  | 
(WIP) |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | System Cost: 11.1201 Avg. WIP: 0.5564 Avg. FG: 1.7400 Lost Sales Rate: 0.1596
 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 
 | 1 | 3 | 3 | 2 | 0 | 0 | 0 | 0 | 
 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 0 | 
 | 3 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 
 | 4 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 
 | 5 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 
 | 6 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | System Cost: 11.1201 Avg. WIP: 0.5564 Avg. FG: 1.7400 Lost Sales Rate: 0.1596
 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 
 | 1 | 3 | 3 | 2 | 0 | 0 | 0 | 0 | 
 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 0 | 
 | 3 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 
 | 4 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 
 | 5 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 
 | 6 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 
Optimal production decisions for both stations
Busy Set
of
Station 1
Busy Set
of
Station 2
However
most of
the states
are
transient
Produce only at
station 1
Produce only at
station 2
Produce at both
stations
S1
S2
WIP
FG

## Slide 23: Numerical Experiments Basic Model with No Rationing
We consider a system with parameters
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | System Cost: 11.1201 Avg. WIP: 0.5564 Avg. FG: 1.7400 Lost Sales Rate: 0.1596
 | 0 | 1 | 1 | 1 | 0 | t | t | t | 
 | 1 | 3 | 3 | 2 | t | t | t | t | 
 | 2 | 2 | 2 | t | t | t | t | t | 
 | 3 | t | t | t | t | t | t | t | 
 | 4 | t | t | t | t | t | t | t | 
 | 5 | t | t | t | t | t | t | t | 
 | 6 | t | t | t | t | t | t | t | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | System Cost: 11.1201 Avg. WIP: 0.5564 Avg. FG: 1.7400 Lost Sales Rate: 0.1596
 | 0 | 1 | 1 | 1 | 0 | t | t | t | 
 | 1 | 3 | 3 | 2 | t | t | t | t | 
 | 2 | 2 | 2 | t | t | t | t | t | 
 | 3 | t | t | t | t | t | t | t | 
 | 4 | t | t | t | t | t | t | t | 
 | 5 | t | t | t | t | t | t | t | 
 | 6 | t | t | t | t | t | t | t | 
Optimal production decisions for both stations
End of
production
at S1
End of
production
at S2
Satisfied
demand
S1
S2
WIP
FG

## Slide 24: Numerical Experiments Basic Model with No Rationing
Now let us define the commonly used policies such as CONWIP, Kanban and Fixed Buffer policies for this system:
CONWIP:
, where is the policy parameter,
Kanban:
,
Fixed Buffer:
, where are the policy parameters, ,

## Slide 25: Numerical Experiments Basic Model with No Rationing
 | CONWIP |  |  |  |  |  | Kanban |  |  |  |  |  | Fixed Buffer |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 |  | 0 | 1 | 2 | 3 | 4 |  | 0 | 1 | 2 | 3 | 4
 | 0 | 1 | 1 | 1 | 0 | t | 0 | 1 | 1 | 1 | 0 | t | 0 | 1 | 1 | 1 | 1 | t
 | 1 | 3 | 3 | 2 | t | t | 1 | 3 | 3 | 2 | t | t | 1 | 2 | 2 | 2 | 0 | t
 | 2 | 3 | 2 | t | t | t | 2 | 3 | 2 | t | t | t | 2 | t | t | t | t | t
 | 3 | 2 | t | t | t | t | 3 | 2 | t | t | t | t | 3 | t | t | t | t | t
 | 4 | t | t | t | t | t | 4 | t | t | t | t | t | 4 | t | t | t | t | t
 | System Cost: 11.15 Avg. WIP: 0.61 Avg. FG: 1.76 Lost Sales Rate: 0.153 |  |  |  |  |  |  | , System Cost: 11.15 Avg. WIP: 0.61 Avg. FG: 1.76 Lost Sales Rate: 0.153 |  |  |  |  |  | , System Cost: 11.88 Avg. WIP: 0.59 Avg. FG: 1.65 Lost Sales Rate: 0.192 |  |  |  | 
 | CONWIP |  |  |  |  |  | Kanban |  |  |  |  |  | Fixed Buffer |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 |  | 0 | 1 | 2 | 3 | 4 |  | 0 | 1 | 2 | 3 | 4
 | 0 | 1 | 1 | 1 | 0 | t | 0 | 1 | 1 | 1 | 0 | t | 0 | 1 | 1 | 1 | 1 | t
 | 1 | 3 | 3 | 2 | t | t | 1 | 3 | 3 | 2 | t | t | 1 | 2 | 2 | 2 | 0 | t
 | 2 | 3 | 2 | t | t | t | 2 | 3 | 2 | t | t | t | 2 | t | t | t | t | t
 | 3 | 2 | t | t | t | t | 3 | 2 | t | t | t | t | 3 | t | t | t | t | t
 | 4 | t | t | t | t | t | 4 | t | t | t | t | t | 4 | t | t | t | t | t
S1
S2
WIP
FG

## Slide 26: Numerical Experiments Effects of holding cost changes
Chart: 
| 1.0 | 1.5 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 4.5 | 5.0
Avg. WIP | 1.0661 | 0.5564 | 0.5564 | 0.5564 | 0.5564 | 0.5564 | 0.5564 | 0.4737 | 0.4737
Avg. FG | 2.0417 | 1.74 | 1.74 | 1.74 | 1.74 | 1.74 | 1.74 | 1.6223 | 1.6223
Chart: 
| 1.0 | 1.5 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 4.5 | 5.0
Lost Sales Rate | 0.1071 | 0.1596 | 0.1596 | 0.1596 | 0.1596 | 0.1596 | 0.1596 | 0.1827 | 0.1827
Cost of holding one unit of WIP inventory on hand
As
System tends to hold less inventory
Therefore more lost sales occur

## Slide 27: Numerical Experiments Effects of the holding cost changes
The cost of holding one unit of FG inventory on hand
As
Less FG inventory causing more lost sales
WIP is not sensitive
The system is more sensitive to compared to
Chart: 
| 1.0 | 1.5 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 4.5 | 5.0
Lost Sales Rate | 0.0674 | 0.0932 | 0.0932 | 0.1127 | 0.1596 | 0.1596 | 0.1596 | 0.1921 | 0.218
Chart: 
| 1.0 | 1.5 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 4.5 | 5.0
Avg. WIP | 0.617 | 0.6532 | 0.6532 | 0.545 | 0.5564 | 0.5564 | 0.5564 | 1 | 0.7744
Avg. FG | 3.0671 | 2.4772 | 2.4772 | 2.2991 | 1.74 | 1.74 | 1.74 | 1.3005 | 1.2331

## Slide 28: Numerical Experiments Effects of the holding cost changes
Total system cost changes according to and
FG inventory holding cost affects the total cost more than WIP does.
Chart: 
h1 | 10.4058 | 10.842 | 11.1201 | 11.3983 | 11.6765 | 11.9547 | 12.2329 | 12.4783 | 12.7152
h2 | 6.324 | 7.8181 | 9.0566 | 10.2201 | 11.1201 | 11.9901 | 12.8601 | 13.6158 | 14.2556

## Slide 29: Numerical Experiments Effects of the production rate changes
Chart: 
| 1.0 | 1.5 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 4.5 | 5.0
Lost Sales Rate | 0.2459 | 0.1688 | 0.1596 | 0.1324 | 0.1162 | 0.1199 | 0.1109 | 0.1044 | 0.0994
Chart: 
| 1.0 | 1.5 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 4.5 | 5.0
Avg. WIP | 0.7342 | 0.7634 | 0.5564 | 0.5812 | 0.5969 | 0.5072 | 0.5117 | 0.5148 | 0.5172
Avg. FG | 1.5229 | 1.7639 | 1.74 | 1.8554 | 1.9321 | 1.896 | 1.9435 | 1.9806 | 2.0103
The production rate of station 1
As increases, the system changes its nature
  [0,2] S1 is the bottleneck
  [2,] S2 is the bottleneck
Effect of is more pronounced when S1 is bottleneck
The inventory is shifted from the buffer to end of line

## Slide 30: Numerical Experiments Effects of the production rate changes
The production rate of station 1
Again bottleneck shifts (This time from S2 to S1)
For small values of , the system cannot attain its desired FG level
Hence initially FG increases and WIP decreases
After the certain speed, the system decides to keep its inventory at the cheaper location
Chart: 
| 1.0 | 1.5 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 4.5 | 5.0
Lost Sales Rate | 0.279 | 0.1643 | 0.1596 | 0.1324 | 0.1162 | 0.1058 | 0.1122 | 0.1026 | 0.0974
Chart: 
| 1.0 | 1.5 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 4.5 | 5.0
Avg. WIP | 1.0427 | 0.729 | 0.5564 | 0.4414 | 0.3635 | 0.3079 | 0.778 | 0.7739 | 0.7479
Avg. FG | 1.4995 | 2.0002 | 1.74 | 1.8554 | 1.9321 | 1.9859 | 1.5206 | 1.5521 | 1.5707

## Slide 31: Numerical Experiments Effects of the production rate changes
Total system cost changes according to and
The system is more sensitive to the rate of S1
This is the opposite of what is observed with holding costs
Chart: 
| 1.0 | 1.5 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 4.5 | 5.0
mu1 | 14.9553 | 12.3871 | 11.1201 | 10.421 | 10.0102 | 9.7488 | 9.4835 | 9.2816 | 9.1289
mu2 | 13.414 | 11.8829 | 11.1201 | 10.7006 | 10.4771 | 10.2989 | 10.1817 | 10.1024 | 10.0466

## Slide 32: Numerical Experiments Effects of the customer arrival rate
The system produces more with the increase of
This also increases both inventory levels initially
However after a certain point, the arrivals eat away the FG
Chart: 
| 0.5 | 1.0 | 1.5 | 2.0 | 2.5 | 3.0
Lost Sales Rate | 0.1228 | 0.1596 | 0.1719 | 0.2445 | 0.3447 | 0.433
Chart: 
| 0.5 | 1.0 | 1.5 | 2.0 | 2.5 | 3.0
Avg. WIP | 0.2193 | 0.5564 | 1.1112 | 1.8482 | 2.5103 | 2.9962
Avg. FG | 1.4386 | 1.74 | 2.2785 | 2.1036 | 1.5632 | 1.1785

## Slide 33: Numerical Experiments Effects of the lost sales cost
As the value of a customer increases,
we observe less lost sales
in order to achieve this, both inventories increases
Chart: 
| 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0
Lost Sales Rate | 0.3077 | 0.1827 | 0.1596 | 0.0932 | 0.0932 | 0.0889 | 0.0618 | 0.0541 | 0.0512
Chart: 
| 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0
Avg. WIP | 0.3462 | 0.4737 | 0.5564 | 0.6532 | 0.6532 | 0.7052 | 1.101 | 0.7301 | 0.7783
Avg. FG | 1 | 1.6223 | 1.74 | 2.4772 | 2.4772 | 2.5158 | 2.8398 | 3.2856 | 3.3321

## Slide 34: Numerical Experiments Basic Model with 2 Customer Classes
 | Optimal Production Decision |  |  |  |  |  | Optimal Rationing Decision |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 |  | 0 | 1 | 2 | 3 | 4 | System Cost: 12.71 Avg. WIP: 0.63 Avg. FG: 2.55 Prob. of Rejecting/Losing Class {1,2} : {0.064, 0.152}
 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 
 | 1 | 3 | 3 | 3 | 2 | t | 1 | 0 | 0 | 1 | 1 | t | 
 | 2 | 3 | 2 | 2 | t | t | 2 | 0 | 1 | 1 | t | t | 
 | 3 | 2 | t | t | t | t | 3 | 0 | t | t | t | t | 
 | 4 | t | t | t | t | t | 4 | t | t | t | t | t | 
 | Optimal Production Decision |  |  |  |  |  | Optimal Rationing Decision |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 |  | 0 | 1 | 2 | 3 | 4 | System Cost: 12.71 Avg. WIP: 0.63 Avg. FG: 2.55 Prob. of Rejecting/Losing Class {1,2} : {0.064, 0.152}
 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 
 | 1 | 3 | 3 | 3 | 2 | t | 1 | 0 | 0 | 1 | 1 | t | 
 | 2 | 3 | 2 | 2 | t | t | 2 | 0 | 1 | 1 | t | t | 
 | 3 | 2 | t | t | t | t | 3 | 0 | t | t | t | t | 
 | 4 | t | t | t | t | t | 4 | t | t | t | t | t | 
We consider a system with parameters
S1
S2
WIP
FG

## Slide 35: Numerical Experiments Basic Model with 2 Customer Classes
Policy | Best Rationing level | Optimal Policy Parameters | Avg. System Cost | Avg. WIP inventory level | Avg. FG inventory level | Prob. of Losing Class 1 Customer | Prob. of Losing/Rejecting Class 2 Customer
Optimal | 2 | - | 12.73 | 0.60 | 2.60 | 0.048 | 0.201
CONWIP | 2 | 4 | 12.81 | 0.68 | 2.64 | 0.046 | 0.192
Kanban | 2 | (4,4) | 12.81 | 0.68 | 2.64 | 0.046 | 0.192
Fixed Buffer | 2 | (2,3) | 13.48 | 1.42 | 2.20 | 0.050 | 0.225
The result of applying four production policies along with the static rationing (IL) policies
CONWIP and Kanban policies are the same here
CONWIP and Kanban are considerably better compared to Fixed Buffer
They increase the inventory levels compared to the optimal

## Slide 36: Numerical Experiments Model with Breakdowns (no rationing)
 | Optimal Production Decision for with breakdowns at both |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6
 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
 | 1 | 3 | 3 | 3 | 3 | 3 | 2 | t
 | 2 | 3 | 3 | 3 | 2 | 2 | t | t
 | 3 | 2 | 2 | 2 | t | t | t | t
 | 4 | t | t | t | t | t | t | t
 | 5 | t | t | t | t | t | t | t
 | 6 | t | t | t | t | t | t | t
 | System Cost: 20.00 |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6
 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
 | 1 | 3 | 3 | 3 | 3 | 3 | 2 | t
 | 2 | 3 | 3 | 3 | 2 | 2 | t | t
 | 3 | 2 | 2 | 2 | t | t | t | t
 | 4 | t | t | t | t | t | t | t
 | 5 | t | t | t | t | t | t | t
 | 6 | t | t | t | t | t | t | t
 | System Cost: 20.00 |  |  |  |  |  |  | 
We consider a system with parameters
 | Optimal Production Decision for the system with no breakdowns |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6
 | 0 | 1 | 1 | 1 | 0 | t | t | t
 | 1 | 3 | 3 | 2 | t | t | t | t
 | 2 | 2 | 2 | t | t | t | t | t
 | 3 | t | t | t | t | t | t | t
 | 4 | t | t | t | t | t | t | t
 | 5 | t | t | t | t | t | t | t
 | 6 | t | t | t | t | t | t | t
 | System Cost: 11.12 |  |  |  |  |  |  | 
 | Optimal Production Decision for the system with no breakdowns |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6
 | 0 | 1 | 1 | 1 | 0 | t | t | t
 | 1 | 3 | 3 | 2 | t | t | t | t
 | 2 | 2 | 2 | t | t | t | t | t
 | 3 | t | t | t | t | t | t | t
 | 4 | t | t | t | t | t | t | t
 | 5 | t | t | t | t | t | t | t
 | 6 | t | t | t | t | t | t | t
 | System Cost: 11.12 |  |  |  |  |  |  | 
 | Optimal Production Decision for with breakdown at S1 |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6
 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 1 | 3 | 3 | 3 | 1 | 1 | 1 | 0
 | 2 | 3 | 3 | 3 | 1 | 0 | 0 | t
 | 3 | 3 | 3 | 3 | 0 | t | t | t
 | 4 | 3 | 3 | 2 | t | t | t | t
 | 5 | 3 | 2 | t | t | t | t | t
 | 6 | 2 | t | t | t | t | t | t
 | System Cost: 17.59 |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6
 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 1 | 3 | 3 | 3 | 1 | 1 | 1 | 0
 | 2 | 3 | 3 | 3 | 1 | 0 | 0 | t
 | 3 | 3 | 3 | 3 | 0 | t | t | t
 | 4 | 3 | 3 | 2 | t | t | t | t
 | 5 | 3 | 2 | t | t | t | t | t
 | 6 | 2 | t | t | t | t | t | t
 | System Cost: 17.59 |  |  |  |  |  |  | 
S1
S2
WIP
FG

## Slide 37: Numerical Experiments Model with Breakdowns (no rationing)
 | Optimal Production Decision for both stations |  |  |  |  |  |  |  | Optimal Production Decision for Station 1 , |  |  |  |  |  |  |  |  | Optimal Production Decision for Station 2 , |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 |  |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 
 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 
 | 1 | 3 | 3 | 3 | 3 | 3 | 2 | t | 1 | 1 | 1 | 1 | 1 | 0 | 0 | t | 1 |  | 2 | 2 | 2 | 2 | 2 | 0 | t | 
 | 2 | 3 | 3 | 3 | 2 | 2 | t | t | 2 | 0 | 0 | 0 | 0 | 0 | t | t | 2 |  | 2 | 2 | 2 | 2 | 2 | t | t | 
 | 3 | 2 | 2 | 2 | t | t | t | t | 3 | 0 | 0 | 0 | t | t | t | t | 3 |  | 2 | 2 | 2 | t | t | t | t | 
 | 4 | t | t | t | t | t | t | t | 4 | t | t | t | t | t | t | t | 4 |  | t | t | t | t | t | t | t | 
 | 5 | t | t | t | t | t | t | t | 5 | t | t | t | t | t | t | t | 5 |  | t | t | t | t | t | t | t | 
 | 6 | t | t | t | t | t | t | t | 6 | t | t | t | t | t | t | t | 6 |  | t | t | t | t | t | t | t | 
 | System Cost: 20.00 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 |  |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 
 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 
 | 1 | 3 | 3 | 3 | 3 | 3 | 2 | t | 1 | 1 | 1 | 1 | 1 | 0 | 0 | t | 1 |  | 2 | 2 | 2 | 2 | 2 | 0 | t | 
 | 2 | 3 | 3 | 3 | 2 | 2 | t | t | 2 | 0 | 0 | 0 | 0 | 0 | t | t | 2 |  | 2 | 2 | 2 | 2 | 2 | t | t | 
 | 3 | 2 | 2 | 2 | t | t | t | t | 3 | 0 | 0 | 0 | t | t | t | t | 3 |  | 2 | 2 | 2 | t | t | t | t | 
 | 4 | t | t | t | t | t | t | t | 4 | t | t | t | t | t | t | t | 4 |  | t | t | t | t | t | t | t | 
 | 5 | t | t | t | t | t | t | t | 5 | t | t | t | t | t | t | t | 5 |  | t | t | t | t | t | t | t | 
 | 6 | t | t | t | t | t | t | t | 6 | t | t | t | t | t | t | t | 6 |  | t | t | t | t | t | t | t | 
 | System Cost: 20.00 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
As the other station breaksdown, the operating one starts to produce less.
S1
S2
WIP
FG

## Slide 38: Future Works
Longer tandem lines (5 stations) in order to investigate the buffer allocation problem from an optimal control perspective
Adaptation to throughput maximization perspective (push) instead of demand satisfaction perspective (pull)
Theoretical characterization of policies